## Slide 1: JPEG2000 Tiles, Subbands, Resolution Levels, Precincts, Code Blocks, etc.
M. A. Mayer
4/11/21

## Slide 2: Image Partitioning (including subbanding)

## Slide 3: Reference Grid and Image Area
Every component, tile, subband, etc. is registered with the overall image via the reference grid.
The reference grid is nothing more than the global coordinate system.
  It defines the origin (0,0)
  It defines the base spatial axes
  Origin is located at top-left corner of the grid
    Increasing X values (columns) go from left to right
    Increasing Y values (rows) go from top to bottom
The Image Area is the portion of the reference grid
that contains imagery
  SIZ marker defines the image area
    Upper left = (XOsiz,YOsiz)
    Lower right = (Xsiz, Ysiz)
(0,0)
(0,0)
(XOsiz,YOsiz)
(Xsiz-1,Ysiz-1)

## Slide 4: Components
A component is exactly that---a self-contained part of the image.
  This is an intentionally vague definition. It allows for whatever use is needed.
  The common theme is that an image is a composite of one or more of its components
Examples:
  Red, Green, Blue bands of an RGB image
  Alpha component as transparency mask
SIZ marker segment
  Each component is same size and location as
    the image area
  Pixel spacing (XRsiz,YRsiz) may be different
    for each component
RGB Image
Red
Green
Blue
(3 components)

## Slide 5: Tiles
Tiles are used to segment the image for compression
  The conversion of image pixels to a JPEG2000 code-stream occurs at the tile level
  The same tiling is used for every component
The tiling
  need not span the entire reference grid
  must span the entire image area
  need not contain the reference grid origin
All tiles
  are of the same size
  must overlap the image area
Tiles are numbered in raster order
SIZ marker segment
  Upper left of 1st tile = (XTOsiz,YTOsiz)
  Tile size = (XTsiz,YTsiz)
Tile 0
Tile 1
Tile 2
Tile 3
Tile 4
Tile 5
Tile 6
Tile 7
Tile 8

## Slide 6: Tile Corner Coordinates
Relative to Reference Grid
  Number rows/columns in the tile grid
  Tile column (p), row (q), and grid (t) indices:
  Upper left corner grid coordinates for each tile
  Lower left corner grid coordinates for each tile
Relative to Component
  Reference grid coordinates scaled by the component pixel spacing

## Slide 7: Discrete Wavelet Transform (DWT)
Before going on to Subbands, we need to discuss the DWT
The DWT splits a signal into high and low frequency signals
  The new signals each contain half as many samples as the original signal
  The low frequency signal contains the coarse form of the original signal
  The high frequency signal contains refining detail
Subsequent DWT iterations can be applied to the low frequency signal
  Results in a lower fidelity signal that still preserves the coarse form of the original signal + a new level of high frequency refinement
Reconstruction of the original signal can be accomplished with Inverse DWT
  Exact reconstruction is possible with lossless wavelet
  Reasonable facsimile is possible with a lossy wavelet

## Slide 8: 2-Dimensional DWT
DWT of a 2D image is accomplished by two passes
  First pass applies DWT to each row
  Second applies DWT to each row
  Result is 4 new 2D ”images” commonly labeled as LL, HL, LH, HH
    L=low frequency, H=high frequency
    1st letter = horizontal band, 2nd letter = vertical band

## Slide 9: Subbands, Decomposition and Resolution Levels
Subbands are result of recursive DWT (discrete waveform transforms)
  Commonly shown composited into a single image
The resolution level is related to the DWT iteration count
  The current DWT iteration is also known as the decomposition level (nb)
  The original image is decomposition level 0
  The final iteration is decomposition level NL
  The resolution level (r) is simply NL – nb
Subbands are labeled using decomposition level and 2D frequency band
Only LL subband that appears in JPEG2000 code-stream is NLLL
  All others can be reconstructed from subsequent resolution level subbands
NL=1
NL=2
NL=3
3LL
3HL
3LH
3HH
2HL
1HL
1HH
1LH
2LH
2HH

## Slide 10: Tile Corner Coordinates (again)
Relative to Resolution Level
  Component coordinates scaled for resolution level spacing
  Mapping between subbands and tiles
    Each resolution level cuts the number of samples by factor of 2
    Physically, subband corners map to to tile corners
    Together, these are equivalent to
  Tile corner coordinates in resolution level coordinates (r)

## Slide 11: Precincts
Precincts are used to partition tiles at the resolution level
  precinct grid origin is coincident with the reference grid origin
  precinct dimensions = 2PPx x 2PPy
  precincts don’t necessarily align with tiles
PPx and PPy can be uniquely specified for
  each tile, component, and resolution level
  At r = 0, PPx and PPy may be 0
  At all other r, PPx and PPy must be > 0
  COD markers
    Scod/SPcod define default (PPx,PPy)
    Can be specified at either file or tile level
  COC markers
    Scoc/SPcoc define component (PPx,PPy) and
      may include distinct values for each resolution level
    Can be specified at either file or tile level
2PPx
2PPy
K0
K1
K2
K3
K4
K5

## Slide 12: Code Blocks
Code blocks are used to partition tiles for coding DWT coefficients
  code block grid origin is coincident with the reference grid origin
  code block dimensions = 2xcb’ x 2ycb’
Precincts contain one or more complete code blocks
  xcb’ = min{ xcb, PPx-1 } for r > 0
  xcb’ = min {xcb, PPx } for r=0
  ycb’ = min{ ycb, PPy-1 } for r > 0
  ycb’ min {ycb, PPy } for r=0
xcb and ycb can be specified differently for each tile and component
  COD markers
    SPcod define default (xcb,ycb)
    Can be specified at either file or tile level
  COC markers
    SPcoc define component (xcb,ycb)
    Can be specified at either file or tile level
code block
precinct

## Slide 13: Code-Stream Formation